## Slide 1
Flipped LED Polarity — Janelia Batch
What's Different
iorodeo panels: Col HIGH + Row LOW = ON
Janelia batch: Col LOW + Row HIGH = ON
Anode/cathode are swapped → current
flows in the opposite direction through
the LED matrix
UCC27517 Driver Impedance
Push-pull output: can source AND sink
R_OH (source) ≠ R_OL (sink)
→ slight asymmetry in drive strength
40 drivers total (20 col + 20 row)
Fully symmetric placement — neither
polarity is disadvantaged
Impact Assessment
Software: Trivial — one XOR per column word + row sense flip. Already implemented.
Voltage droop: Active row carries 20× single-LED current. With reversed polarity, row pin SOURCES
(vs sinks in normal). UCC27517 R_OH may be slightly higher than R_OL → marginally more droop.
Practical effect expected to be small given UCC27517's low output impedance (~1Ω typ).

## Slide 2
Route EINT to MCU
Current State
EINT on headers J3-1 and J5-1
NOT routed to any MCU GPIO
GP45, GP46, GP47 are unconnected
Fix: Add One PCB Trace
Route EINT header → GP45
No rerouting of existing signals
Break out GP46-47 to test points
Arena controller: zero changes
What This Enables
GP45 — EINT (external trigger input)
2P microscope sync: 8 kHz trigger from scan mirror
Already tested with bodge wire: zero jitter confirmed
GP46 — Sync output (burst active)
HIGH during ~10 µs scan burst → oscilloscope/Saleae timing verification
GP47 — Frame-sync / spare
Pulse per frame (400 Hz) or general debug

## Slide 3
Board Size — 45.0 × 45.0 mm
From KiCad PCB
Edge.Cuts: (50,50) → (95,95)
Width: 45.0 mm
Height: 45.0 mm
Square outline
Components
RP2354 MCU (RP2350 + 8MB PSRAM)
40× UCC27517 gate drivers
20×20 passive LED matrix
SPI + EINT headers
2MB flash

## Slide 4
Optimize GPIO for PIO — Contiguous Rows
Current Layout
GP1-20 Columns (contiguous) ✓
GP21-31 Rows lower (11 pins)
GP32-35 SPI0 ← GAP!
GP36-44 Rows upper (9 pins)
GP45-47 Unconnected
⚠ SPI pins break row range
Cannot use PIO for rows
Proposed (Option C)
GP1-20 Columns → PIO0
GP21-40 Rows → PIO1 ✓
GP41 EINT trigger
GP42-43 Sync + spare
GP44-47 SPI1 (hardware)
✓ Both ranges contiguous
Enables fully autonomous PIO scan
What Contiguous Rows Enable
PIO1 out pins, 20 for rows — entire scan burst can be PIO-only (zero CPU in loop)
PIO1 wait pin on GP41 — hardware trigger with zero CPU latency
No funcsel conflicts — SPI1 (GP44-47) completely outside PIO row range
Firmware: spi_init(spi0,...) → spi_init(spi1,...) + update pin constants. One-line change.