## Slide 1
G6 20×20 LED Panel
Timing, Grayscale & Linearity Characterization
RP2354 MCU (150 MHz)
PIO-driven BCM
Zero-jitter architecture
Spectrometer-calibrated
Reiser Lab — March 2026

## Slide 2
Zero-Jitter BCM Architecture
0.000 µs
Jitter
640k measurements
9.5 µs
Burst time
5.5 µs margin in 15 µs
400 Hz
Frame rate
8 kHz ÷ 20 rows
Zero-Jitter Recipe
__not_in_flash_func + noinline
noInterrupts() during burst
multicore_lockout (Core 1)
100-trigger warm-up
Architecture
4-bit BCM: 16 intensity levels
PIO drives 20 columns simultaneously
CPU manages rows (gpio_set_mask64)
Single row per 8 kHz trigger
External trigger on GP45 (zero jitter)

## Slide 3
BCM Waveform — Pulse-Triggered Average
Key Observations
499 pulses averaged
50 MHz analog capture
4 bit-planes resolved:
B0: 0.5µs B1: 1.0µs
B2: 2.0µs B3: 4.0µs
~0.4µs PIO overhead gaps between bit-planes
Peak amplitude decreases
with each successive
bit-plane — key finding
for linearity calibration
Photodiode signal via Saleae Logic Pro 8 analog input

## Slide 4
BCM Linearity — Default Weights [1, 2, 4, 8]
Ocean Insight Flame X Spectrometer
LED peak: 570.8 nm
Integration: 50ms | Window: 560-580nm (20nm)
T = 0.7 µs | All 400 LEDs | DWT trigger
NOT monotonic
Max error: 6.7%
Problem: L3 ≈ L4, L7 > L8, L11 ≈ L12
Bit-plane boundaries are non-monotonic
Root cause: brightness per µs decays
B0: 3163 cts/µs
B1: 2648 cts/µs (−16%)
B2: 2108 cts/µs (−33%)
B3: 2024 cts/µs (−36%)
Measured vs Ideal
Lv | Measured | Ideal | Err
0 | 0.000 | 0.000 | +0.0%
1 | 0.100 | 0.067 | +3.4%
2 | 0.168 | 0.133 | +3.4%
3 | 0.267 | 0.200 | +6.7%
4 | 0.267 | 0.267 | +0.0%
5 | 0.365 | 0.333 | +3.1%
6 | 0.430 | 0.400 | +3.0%
7 | 0.526 | 0.467 | +5.9%
8 | 0.513 | 0.533 | -2.1%
9 | 0.607 | 0.600 | +0.7%
10 | 0.671 | 0.667 | +0.4%
11 | 0.764 | 0.733 | +3.1%
12 | 0.761 | 0.800 | -3.9%
13 | 0.853 | 0.867 | -1.4%
14 | 0.913 | 0.933 | -2.1%
15 | 1.000 | 1.000 | +0.0%
← Non-monotonic pairs highlighted

## Slide 5
BCMWEIGHTS Optimization — Converged in 6 Iterations
Iter | B0 | B1 | B2 | B3 | Mono? | Max Err
0 | 1.00 | 2.00 | 4.00 | 8.00 | NO | 6.7%
1 | 1.00 | 2.00 | 4.00 | 8.69 | NO | 5.4%
2 | 1.00 | 2.00 | 4.66 | 8.69 | NO | 5.5%
3 | 1.00 | 2.00 | 4.66 | 9.41 | YES | 3.5%
4 | 1.00 | 2.00 | 4.66 | 9.80 | YES | 3.0%
5 | 1.00 | 2.00 | 5.02 | 9.80 | YES | 3.4%
6 | 1.00 | 2.00 | 5.02 | 10.19 | YES | 2.5%
Key Insight
Only B2 and B3 needed adjustment
B0, B1 unchanged at 1, 2
B2: 4.00 → 5.02 (+26%)
B3: 8.00 → 10.19 (+27%)
Compensates for
brightness-per-µs decay
in longer bit-planes
Before → After
Level | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Before | 0% | 3% | 3% | 7% | 0% | 3% | 3% | 6% | -2% | 1% | 0% | 3% | -4% | -1% | -2% | 0%
After | 0% | 2% | 1% | 2% | 1% | 2% | 1% | 3% | 1% | 2% | 1% | 2% | -0% | 1% | -1% | 0%
NOT monotonic, 6.7% error
MONOTONIC, 2.5% error ✓

## Slide 6
Timing Budget — Production Configuration
Config | T (µs) | Weights | Burst (µs) | Margin | Monotonic | Error
Default | 0.50 | 1, 2, 4, 8 | 9.46 | 5.5 µs | —* | —*
Default | 0.70 | 1, 2, 4, 8 | 12.1 | 2.9 µs | NO | 6.7%
Optimized | 0.70 | 1, 2, 5.0, 10.2 | 12.7 | 2.3 µs | YES | 2.5%
Default | 1.00 | 1, 2, 4, 8 | 16.96 | −2.0 µs | YES | 5.6%
Recommended: T=0.7µs + optimized weights
*T=0.5 linearity not yet measured with spectrometer (too dim for full-panel test)
8 kHz Trigger Period (125 µs)
Burst 12.7µs
Idle: 112.3 µs — SPI, precompute, interrupts

## Slide 7
Next Steps
Reverse Bit-Plane Order
BCMORDER REVERSE: scan B3→B0
Test if longest-first improves linearity
Compare with spectrometer + photodiode
May eliminate need for weight calibration
Single LED vs Full Row
Measure 1 LED → 5 → 10 → 20 → 400
Test current-sharing / voltage-drop effects
May explain brightness-per-µs decay
Focal LED on row 7 (nearest to fiber)
PCB Redesign
Option B: add EINT trace to GP45
Option C: SPI1 on GP44-47, contiguous rows
40 UCC27517 drivers symmetric (both sides)
EINT + sync output pins on next revision
Production Path
Per-pixel pattern loading via SPI
Frame double-buffering at 400 Hz
BCMWEIGHTS calibration per panel
PIO wait-pin for hardware trigger